## Slide 1: MAC Addressing

## Slide 2: MAC Address
A Media Access Control (MAC) address is a unique identifier assigned to a network interface for communication on a physical network.
It is a 48-bit hexadecimal code, typically represented as six groups of two digits, used for device identification and addressing in data transmission.

## Slide 3: Features of MAC Address
Uniqueness: Each MAC address is globally unique, ensuring no two devices share the same identifier.
Fixed Length: Consists of a fixed number of bits (48 bits for most MAC addresses).
Device Identification: Identifies network interfaces, allowing for device recognition on a network.
Hard-Coded: Often burned into the network interface hardware during manufacturing.
Link-Layer Communication: Essential for addressing and communication at the link layer of the OSI model.

## Slide 4: Features of MAC Address
Non-Routable: Typically not used for routing decisions; operates at the local network level.
Hexadecimal Representation: Expressed in base-16 format for human readability.
Assigned by IEEE: The first half of the MAC address (24 bits) is assigned to manufacturers by the Institute of Electrical and Electronics Engineers (IEEE).
Static: Generally remains constant throughout the device's lifetime.
Broadcast Filtering: Used in switches and routers to filter and forward data based on MAC addresses.

## Slide 5: Importance of MAC
Network Device Identification: MAC addresses uniquely identify network interfaces, enabling devices to recognize and communicate with each other on a local network.
Security: MAC addresses are used in network access control lists (ACLs) to restrict or allow access to a network, enhancing security by permitting or denying specific devices.

## Slide 6: Importance of MAC
Switching and Routing: MAC addresses play a crucial role in local switching decisions within network switches, facilitating efficient data transmission within the same network segment.
Device Tracking: MAC addresses aid in tracking and managing devices on a network. This is particularly valuable for troubleshooting, monitoring, and optimizing network performance.
DHCP (Dynamic Host Configuration Protocol): MAC addresses are used in DHCP to dynamically assign IP addresses to devices on a network. This ensures that each device receives a unique IP address during the DHCP process, promoting efficient network resource utilization.

## Slide 7: DHCP
Dynamic Host Configuration Protocol (DHCP) is a network protocol that automatically assigns IP addresses and network configuration information to devices within a local network.
It streamlines the process, ensuring devices receive unique addresses, simplifying network management and enabling seamless connectivity without manual IP configuration.

## Slide 8: DHCP understanding
Imagine DHCP as a helpful server in a neighborhood assigning unique parking spots (IP addresses) to cars (devices).
Instead of drivers choosing spots, the DHCP server automatically gives each car its own designated parking space, making it easier for everyone to find and connect without confusion.

## Slide 9: MAC Addressing
What is MAC Addressing?
MAC addressing refers to the process of assigning unique identifiers, known as Media Access Control (MAC) addresses, to network interfaces on devices. These addresses enable devices to communicate and identify each other on a local network.

## Slide 10: How it Works
Uniqueness: MAC addresses are globally unique, preventing two devices from having the same identifier.
Hardware-assigned: Typically embedded in the network interface hardware during manufacturing.
Layer 2 Communication: Operates at the data link layer, facilitating communication within the same local network segment.
Hexadecimal Representation: Expressed in a 48-bit hexadecimal format for human readability.

## Slide 11: what if MAC addressing not used?
Device Identification: Without MAC addresses, devices on a network would lack unique identifiers, making it challenging for them to communicate and be recognized by other devices.
Address Resolution: MAC addresses play a key role in address resolution protocols, such as ARP (Address Resolution Protocol), which maps IP addresses to MAC addresses. Without MAC addressing, these protocols would be ineffective.

## Slide 12: what if MAC addressing not used?
Switching Decisions: Network switches rely on MAC addresses to make forwarding decisions within a local network. Without MAC addressing, switches would struggle to efficiently direct data to the appropriate devices.
Security Measures: MAC addresses are often used in access control lists (ACLs) for security purposes. Without MAC addressing, the ability to control and restrict network access based on device identity would be compromised.
DHCP Functionality: Dynamic Host Configuration Protocol (DHCP) relies on MAC addresses to dynamically assign IP addresses to devices. Without MAC addressing, DHCP would be less effective, and manual IP address configuration might be required.

## Slide 13: How to do MAC addressing?
MAC addressing is typically assigned to network interfaces during the manufacturing process of the network interface card (NIC) or network adapter.
However, in some cases, you may need to modify or configure MAC addresses manually. Here's how you can do it:

## Slide 14: How to do MAC addressing?(windows)
Change MAC Address Using Device Manager:
Open Device Manager.
Locate and right-click on your network adapter.
Choose "Properties" and go to the "Advanced" tab.
Look for an option like "Network Address" or "Locally Administered Address."
Enter the new MAC address and click "OK."

## Slide 15: How to do MAC addressing?(windows)
Change MAC Address Using Command Prompt:
Open Command Prompt with administrator privileges.
Type ipconfig /all to display your current MAC address.
Type netsh interface set interface "Your Network Interface Name“
newmac=XX-XX-XX-XX-XX-XX to change the MAC address.