## Slide 1: Network Devices
Lecture 6

## Slide 2: Network Devices
Network devices, also known as networking hardware, are physical devices that allow hardware on a computer network to communicate and interact with one another.
For example Repeater, Hub, Bridge, Switch, Routers, Gateway, Brouter, and NIC, etc.

## Slide 3: Repeater
A repeater operates at the physical layer.
A repeater is like a booster for network signals. It takes weak signals and makes them stronger so they can travel longer distances. Think of it as a friendly echo that helps your messages go further, ensuring everyone in the network can hear each other loud and clear.
An important point to be noted about repeaters is that they not only amplify the signal but also regenerate it.
It is a 2-port device.

## Slide 4: Hub
A hub is like a busy town square where everyone gathers.
It connects different devices in a network so they can talk to each other.
When one device sends a message, the hub sends it to all the other devices. It's like a helpful messenger making sure everyone gets the news.
They do not have the intelligence to find out the best path for data packets which leads to inefficiencies and wastage.

## Slide 5: Types of hub
Active Hub:- These are the hubs that have their power supply and can clean, boost, and relay the signal along with the network. It serves both as a repeater as well as a wiring center. These are used to extend the maximum distance between nodes.
Passive Hub:- These are the hubs that collect wiring from nodes and power supply from the active hub. These hubs relay signals onto the network without cleaning and boosting them and can’t be used to extend the distance between nodes.
Intelligent Hub:- It works like an active hub and includes remote management capabilities. They also provide flexible data rates to network devices. It also enables an administrator to monitor the traffic passing through the hub and to configure each port in the hub

## Slide 6: Bridge
A bridge is like a smart traffic wardon for data.
It helps direct information in a network to the right place.
Imagine it as a bridge over a river, ensuring that cars (data) go to the correct destination without getting lost.
This makes networks work faster and more efficiently.
A bridge is a repeater, with add on the functionality of filtering content by reading the MAC addresses of the source and destination.
It is also used for interconnecting two LANs working on the same protocol. It has a single input and single output port, thus making it a 2 port device.

## Slide 7: Types of Bridge
Transparent Bridges:- These are the bridge in which the stations are completely unaware of the bridge’s existence i.e. whether or not a bridge is added or deleted from the network, reconfiguration of the stations is unnecessary. These bridges make use of two processes i.e. bridge forwarding and bridge learning.
Source Routing Bridges:- In these bridges, routing operation is performed by the source station and the frame specifies which route to follow. The host can discover the frame by sending a special frame called the discovery frame, which spreads through the entire network using all possible paths to the destination.

## Slide 8: Switch
A switch is a multiport bridge with a buffer and a design that can boost its efficiency(a large number of ports imply less traffic) and performance. A switch is a data link layer device.
The switch can perform error checking before forwarding data, which makes it very efficient as it does not forward packets that have errors and forward good packets selectively to the correct port only.

## Slide 9: Types of Switches
Unmanaged switches: These are basic switches that work out of the box without any configuration. They're like plug-and-play devices, making them easy to use but with fewer customization options.
Managed switches: Managed switches offer more control and customization. They allow you to configure settings, monitor traffic, and perform other advanced tasks. They're like having a control panel for your network.
Smart switches: Smart switches are a middle ground between unmanaged and managed switches. They offer some customization options but are simpler to set up than fully managed switches.

## Slide 10: Types of Switches
Layer 2 switches: These switches operate at the Data Link Layer (Layer 2) of the OSI model. They use MAC addresses to forward data packets within a local network. They're like traffic managers for devices within the same area.
Layer 3 switches: Layer 3 switches operate at the Network Layer (Layer 3) of the OSI model. They can make routing decisions based on IP addresses, allowing them to connect different networks. They're like advanced traffic managers that can handle inter-network traffic.
PoE switches: Power over Ethernet (PoE) switches can supply power to devices like IP cameras and phones through the same Ethernet cable used for data. They're like electrical outlets and data ports rolled into one.

## Slide 11: Types of Switches
Gigabit switches: These switches support faster data transfer speeds, typically 1 gigabit per second. They're like high-speed highways for data within a network.
Rack-mounted switches: These switches are designed to be installed in a standard equipment rack. They're like neatly organized shelves for network devices in a data center.
Desktop switches: These switches are compact and designed to sit on a desk or tabletop. They're suitable for smaller networks and offices.
Modular switches: Modular switches allow you to customize and expand your network by adding or removing modules for specific functionalities. They're like building blocks for a tailored network infrastructure.

## Slide 12: Router
A router is a device like a switch that routes data packets based on their IP addresses.
The router is mainly a Network Layer device.
Routers normally connect LANs and WANs and have a dynamically updating routing table based on which they make decisions on routing the data packets.
The router divides the broadcast domains of hosts connected through it.

## Slide 13: Gateway
A gateway is like a door to another world in a network.
It's a special device that connects different networks, like your home network to the internet.
It knows the way in and out, helping data find its destination. Think of it as a bridge between your local network and the wider world of the internet.

## Slide 14: Brouter
It is also known as the bridging router is a device that combines features of both bridge and router.
It can work either at the data link layer or a network layer. Working as a router, it is capable of routing packets across networks and working as the bridge, it is capable of filtering local area network traffic.

## Slide 15: NIC
NIC or network interface card is a network adapter that is used to connect the computer to the network. It is installed in the computer to establish a LAN.
It has a unique id that is written on the chip, and it has a connector to connect the cable to it. The cable acts as an interface between the computer and the router or modem.
NIC card is a layer 2 device which means that it works on both the physical and data link layers of the network model.