## Slide 1: Random Access Protocols(cont)
Lecture 14

## Slide 2: CSMA
Carrier Sense Multiple Access (CSMA) is a network protocol used in computer networks to control access to a shared communication medium, such as a network segment or a wireless channel.
In CSMA, a device listens to the communication channel before transmitting data to ensure that it is clear. If the channel is busy, the device waits until it is idle before attempting to transmit.
This method helps prevent data collisions and improves the efficiency of communication on a shared network.

## Slide 3: CSMA working Example
Imagine CSMA like a group discussion where people wait for a pause before speaking. Here's a simple analogy:
In a meeting, before someone starts talking, they first check if others are speaking. If it's quiet, they speak up. If someone else is talking, they patiently wait for the conversation to finish.
This courteous approach is similar to how CSMA works in a network—devices listen to the communication channel and wait for an opportunity to transmit without causing interference.

## Slide 4: CSMA/CD
CSMA/CD, or Carrier Sense Multiple Access with Collision Detection, is a network protocol used in Ethernet networks to manage access to a shared communication medium.In CSMA/CD, devices listen to the network before transmitting to check for activity.
If the channel is clear, they send their data. However, if a collision is detected (two devices transmitting simultaneously, causing interference), both devices stop transmitting, wait for a random period, and then attempt to resend. CSMA/CD was commonly used in traditional Ethernet networks but has become less relevant with the widespread adoption of full-duplex Ethernet.

## Slide 5: CSMA/CD Working
Imagine a group of friends having a conversation. They follow a CSMA/CD-like protocol:
1. Listen: Before speaking, each friend listens to make sure no one else is talking.
2. Speak: If it's quiet, they speak up and share their message.
3.Collision: If two friends accidentally start talking at the same time, they both stop, wait for a moment, and then try again.
In the context of CSMA/CD in networking, it's like computers checking if the network is clear before sending data. If two computers try to send data simultaneously and a collision occurs, they pause, wait for a random time, and then attempt to resend to avoid further collisions.

## Slide 6: CSMA/CA
CSMA/CA, or Carrier Sense Multiple Access with Collision Avoidance, is a network protocol commonly used in wireless networks like Wi-Fi.
In CSMA/CA, devices listen to the wireless channel to check for ongoing transmissions before attempting to send data. If the channel is clear, they send a request to transmit.
The device waits for acknowledgment from the receiver before proceeding with data transmission, helping to avoid collisions in the wireless environment. This protocol is particularly useful in scenarios where collision detection (as in CSMA/CD) is less practical, such as in wireless communication.

## Slide 7: Working Example of CSMA/CA
Think of CSMA/CA like a group discussion where people raise their hands before talking to avoid talking over each other. Here's a simple analogy:
1.Listen and Raise Hand: Imagine friends in a circle. Before speaking, each friend looks around to ensure nobody else is talking. If it's quiet, they raise their hand to signal they want to talk.
2. Acknowledgment: Others in the group observe the raised hand and acknowledge the person who wants to speak. This acknowledgment ensures everyone is aware and ready for the upcoming conversation.
3. Speak: Once acknowledged, the person speaks without worrying about someone else talking at the same time.
In the context of CSMA/CA in wireless networks, devices "listen" to the channel, send a request to transmit, wait for acknowledgment, and then proceed with data transmission to avoid collisions in the wireless environment.