## Slide 1: Channelization protocols
Lecture 15

## Slide 2: Channelization Protocol
Channelization protocols refer to communication schemes that divide a communication medium, such as a frequency band, into multiple channels.
These protocols facilitate the simultaneous transmission of multiple independent signals within the same overall bandwidth. Channelization helps optimize the use of available resources, reducing interference between communication streams.
Common examples include Frequency Division Multiple Access (FDMA) and Time Division Multiple Access (TDMA) protocols in telecommunications.

## Slide 3: Frequency Division Multiple Access (FDMA)
FDMA (Frequency Division Multiple Access) is a communication protocol that divides the available frequency spectrum into distinct channels.
Each channel is allocated to a specific user, allowing multiple users to communicate simultaneously without interference.
It is commonly used in radio and telecommunications systems.

## Slide 4: Frequency Division Multiple Access (FDMA)
Frequency Division Multiple Access (FDMA) is like a radio station concept for communication. Imagine a radio dial where each station occupies a specific frequency.
In FDMA, different users or conversations are like separate radio stations, each assigned its unique frequency "channel." This way, multiple conversations can happen at the same time without interference because they're using different frequencies.
It's a bit like tuning in to different radio stations to hear different things, but applied to communication systems like mobile phones where each user gets its own frequency channel for clear and simultaneous communication.

## Slide 5: TDMA
Time Division Multiple Access (TDMA) is a communication protocol that divides a communication channel into time slots.
Each user is assigned a specific time slot during which they can transmit and receive data. This allows multiple users to share the same frequency without overlapping, making efficient use of the available bandwidth.
TDMA is commonly used in mobile and digital communication systems, where each user gets dedicated time intervals for communication within a defined cycle.

## Slide 6: CDMA
Code Division Multiple Access (CDMA) is a digital communication technology that allows multiple users to share the same frequency band simultaneously.
In CDMA, each user's signal is uniquely encoded with a specific code, and all users transmit in the same frequency range simultaneously.
The receiver uses the codes to separate and distinguish between the different signals, enabling multiple users to communicate concurrently on the same channel. CDMA is a widely used technology in mobile communication systems.

## Slide 7: CDMA
Code Division Multiple Access (CDMA) is like a crowded party where everyone is talking at the same time, but each person has a unique language that only their intended listener understands.
In CDMA, multiple users share the same frequency at the same time, but they use different codes to keep their conversations separate. It's a way for many people to communicate simultaneously without talking over each other, like having private conversations in a noisy room.